## Slide 1
Day 2: Characterization of the local field potential and its relation to spiking activity
Junji Ito | Institute of Neuroscience and Medicine (INM-6) and Institute for Advanced Simulation (IAS-6), Jülich Research Centre and JARA, Jülich, Germany
SPP 1665 Analytical Workshop: Analysis and Management of Electrophysiological Activity Data
Forschungszentrum Jülich, Jülich, Germany (Nov. 24-27, 2014)

## Slide 2
Introduction
  What is LFP? | LFP origin | oscillations in LFP
Spectral Analysis
  Fourier transform | power spectrum | coherency
Phase Locking Analysis
  Hilbert transform | wavelet transform | phase locking value
Spike-LFP Relation
  spike triggered average | spike field coherence | period histogram | vector strength
Outline

## Slide 3
Local field potential (LFP) is…
  electric potential  high temporal resolution
  measured within the brain using microelectrodes  high spatial resolution
  caused (primarily) by excitatory synaptic currents of nearby neurons  reflection of inputs to the local neuronal circuit
Introduction | what is local field potential?
Varela et al. (2001) Nat. Rev. Neurosci. 2:229–39

## Slide 4
LFP is the low-pass filtered voltage signal
Introduction | how to obtain the LFP?

## Slide 5
Under assumptions of...
  Quasi-static (< 1 kHz) electric field (= capacitive and inductive effects are negligible)
  Isotropic extracellular medium (= conductance is a constant scalar, instead of a tensor)
  Field potential is dependent only on the magnitudes and positions of current sources
What causes current sources in the extracellular space?  transmembrane currents of neurons
Introduction | what is the origin of the LFP?
: field potential at : current source at : conductance of extracellular medium

## Slide 6
Action potentials (APs)
  Biphasic in time, easily cancelled out by temporal jitter of multiple APs
Excitatory and inhibitory post-synaptic potentials (EPSP, IPSP)
  Ratio of EPSP- vs. IPSP-related current components = 5:1 (Mitzdorf, 1985)
EPSP is the dominant cause of the macroscopic transmembrane current (and therefore the LFPs) in the brain.
Introduction | cause of transmembrane current
Mitzdorf (1985) Physiol. Rev. 65:37-100

## Slide 7
A cell is always electrically neutral  current sink is cell-wise counter-balanced by current source
Spatial distribution of sinks and sources depends on cell shapes
  Overlapping current sinks and sources cancel each other
  Only localized current sinks and sources contribute to macroscopic LFP
Excitatory synaptic inputs to pyramidal neurons contribute most to the cortical LFP
Introduction | cell morphology and LFP

## Slide 8
Laminar LFP recording from the area IT of an anesthetized macaque (data by courtesy of Prof. Tamura, Osaka Univ.)
Introduction | an example LFP recording
LFP movie

## Slide 9
Ubiquitous oscillations in LFP
  in both response and ongoing activity
  in a wide range of frequency
Introduction | oscillations in LFP
Ito et al. (2014) Nat. Commun. 5:3572
Fries et al. (2001). Science 291:1560–3
Macaque V4
Spaak et al. (2012) Curr. Biol. 2:2313–8
Macaque V1
Mouse barrel cortex

## Slide 10
Introduction
  What is LFP? | LFP origin | oscillations in LFP
Spectral Analysis
  Fourier transform | power spectrum | coherency
Phase Locking Analysis
  Hilbert transform | wavelet transform | phase locking value
Spike-LFP Relation
  spike triggered average | spike field coherence | period histogram | vector strength
Outline

## Slide 11
Sinusoid:
Spectral Analysis | representation of oscillation
Phase offset:
Amplitude:
Cycle and frequency:
Time
Phase difference:

## Slide 12
Decomposition into sinusoids
Spectral Analysis | Fourier transform
time-varying signal (real-valued scalar)
Fourier transform of
Amplitude
Phase
f-Hz sinusoid of amplitude and phase-offset
is a complex function of frequency :
(Inverse Fourier transform)

## Slide 13
Estimation of power spectral density (PSD)
  Periodogram:
  Welch’s method
    Cut a signal into segments of an identical length
    Multiply the segments by a window function (edge smoothing)
    Compute periodograms of the segments and average them
Spectral Analysis | power spectrum

## Slide 14
A measure of correlation between spectral components in two signals
  Signals:
  Cross-periodogram:
  Cross-spectrum
    Estimated from the cross-periodograms of signal segments by Welch’s method
Spectral Analysis | cross-spectrum
Phase difference
: average over segments by Welch’s method
Phase cross-spectrum (average phase difference)
Amplitude cross-spectrum

## Slide 15
Amplitude cross-spectrum
  takes values between 0 and , depending on the phase coherency between the signals and at frequency
Coherency
  cross-spectrum normalized by auto-spectra (= power spectra) of the original signals
Spectral Analysis | coherency
perfect coherence at frequency
independence

## Slide 16
Introduction
  What is LFP? | LFP origin | oscillations in LFP
Spectral Analysis
  Fourier transform | power spectrum | coherency
Phase Locking Analysis
  Hilbert transform | wavelet transform | phase locking value
Spike-LFP Relation
  spike triggered average | spike field coherence | period histogram | vector strength
Outline

## Slide 17
Spectral analysis yields measures in the frequency domain
  No direct insights into signals’ behavior in the time domain
  Assumption: signals are stationary in time
In reality, neuronal signals are highly nonstationary
  Stimuli are typically not constantly presented but only at specific times (“trials”)
  Even without external stimuli, spontaneous activities of neuronal systems are not stationary, but highly irregular
Need for time-resolved spectral analysis
  In concrete, methods to estimate instantaneous amplitude and phase of oscillatory signals  Hilbert transform, wavelet transform
Phase Locking Analysis | motivation

## Slide 18
Convolution of and :
Convolution theorem
  Fourier transform of the convolution of and is the (frequency-wise) product of Fourier transforms of and
  You can compute convolution by 1) Fourier transform the functions, 2) multiply them frequency-wise, and 3) inverse Fourier transform the product
Phase Locking Analysis | convolution theorem
convolution
frequency-wise multiplication

## Slide 19
Hilbert transform of :
  convolution with in the time domain represents radian rotation in the frequency domain
  By Hilbert transform, each and every frequency component of is phase-shifted by radian
Phase Locking Analysis | Hilbert transform
Example: multiplication by and

## Slide 20
Analytic signal: complex signal of which imaginary part is Hilbert transform of its real part (i.e., )
  Example: complex sinusoid
  Amplitude and phase of analytic signal are defined as:
  For any real-valued signal , a corresponding analytic signal can be constructed by Hilbert transform
  This enables estimation of instantaneous amplitude and phase at any time
Phase Locking Analysis | analytic signal

## Slide 21
Time- and frequency-resolved decomposition
Phase Locking Analysis | wavelet transform
time-varying signal (real-valued scalar)
wavelet transform of the signal
f-Hz sinusoid
Gaussian of width centered at
Le van Quyen et al. (2001) J. Neurosci. Meth. 111:83-98
Morlet wavelet
(5 cycles in )

## Slide 22
How wavelet transform works
Phase Locking Analysis | wavelet transform

## Slide 23
Estimation with wavelet transform
Phase Locking Analysis | phase estimation
LFP (uV)
Amp.
Phase
WT (A.U.)

## Slide 24
Instantaneous phase difference as a time-resolved measure of correlation between oscillatory signals
Constant phase difference over a period of time  phase locking
Phase locking value (PLV) for and
Phase Locking Analysis | phase locking value
Varela et al. (2001) Nat. Rev. Neurosci. 2:229–39

## Slide 25
Rodriguez et al. (1999), EEG recording from human subjects
Viewing of “Face” and “Nonsense” images
Phase locking analysis over a range of frequencies (20 – 60 Hz)
High PLVs at ~40 Hz only in Face viewing condition
Phase Locking Analysis | an example application
Varela et al. (2001) Nat. Rev. Neurosci. 2:229–39

## Slide 26
Introduction
  What is LFP? | LFP origin | oscillations in LFP
Spectral Analysis
  Fourier transform | power spectrum | coherency
Phase Locking Analysis
  Hilbert transform | wavelet transform | phase locking value
Spike-LFP Relation
  spike triggered average | spike field coherence | period histogram | vector strength
Outline

## Slide 27
Montemurro et al. (2008), recording from V1 of anesthetized macaques
Repeatedly stimulated with a natural movie
Reliable oscillatory LFP responses across trials
How are spike timings related to the phase of LFP oscillations? How to quantify the relation?
Spike-LFP Relation | spike-LFP parallel recording
Montemurro et al. (2008) Curr. Biol. 18:375–80

## Slide 28
Average of LFP segments with spike times as triggers
If spikes prefer a specific phase of the LFP oscillation, its oscillatory waveform would remain in the average, while random fluctuations would be averaged out
...but, how can one tell if an obtained STA reflects phase locking or remaining fluctuations?  need for significance test
Spike-LFP Relation | spike triggered average

## Slide 29
Spike time randomization for significance test
  Generate a surrogate spike data by randomly shuffling spike times
  Compute STA using the surrogate spike data and the original LFP data
  Repeat 1 and 2 many times (typically > 1,000)
  Compute the distribution of surrogate STAs, and test the significance of the original STA against it
Spike-LFP Relation | significance test

## Slide 30
STA can give a spurious result when the LFP has large power in other frequencies than the one that spikes are related to
In such cases, STA needs to be “normalized” by the power in each frequency  Spike-field coherence (SFC)
Spike-LFP Relation | spike-field coherence
Fries et al. (2002) J. Neurosci 22:3739-54

## Slide 31
SFC is...
  defined as the power spectrum of STA divided by the power spectrum of the LFP
  a measure in the frequency domain
  a normalized measure taking a value between 0 and 1 for each frequency (0: independence; 1: perfect coherence)
  actually coherency between spike train and LFP (with spike train represented as sum of delta peaks)
Spike-LFP Relation | spike-field coherence
Fries et al. (2002) J. Neurosci 22:3739-54
STA
PSD of STA
PSD of LFP
SFC

## Slide 32
Chalk et al. (2010), recording from V1 and V4 of awake behaving macaques
SFC reflects attentional state of the animal
Spike-LFP Relation | an example application
Chalk et al. (2010) Neuron 66:114-25

## Slide 33
Phase extraction enables characterization of spike-LFP relation with a fine temporal resolution
What phase do spikes prefer? How are spike times distributed across phases within a cycle?  period histogram
Spike-LFP Relation | phase locking analysis
Montemurro et al. (2008) Curr. Biol. 18:375–80

## Slide 34
Simultaneously recorded LFP and spikes
  LFP:
  spike times:
Phases at spike times:
Histogram of is called period histogram
Spike-LFP Relation | period histogram
Denker et al. (2011) Cereb. Cortex 21:2681-95

## Slide 35
Vector strength (or mean vector length):
  c.f. (LFP-to-LFP) phase locking value
  Quantifies the degree of spike-to-LFP phase locking
Spike-LFP Relation | vector strength
perfect phase locking
independence

## Slide 36
Denker et al. (2011), recording from M1 of awake behaving macaques (note: circular std. dev. )
Spike-LFP Relation | an example application
Denker et al. (2011) Cereb. Cortex 21:2681-95

## Slide 37
Introduction
  What is LFP? | LFP origin | oscillations in LFP
Spectral Analysis
  Fourier transform | power spectrum | coherency
Phase Locking Analysis
  Hilbert transform | wavelet transform | phase locking value
Spike-LFP Relation
  spike triggered average | spike field coherence | period histogram | vector strength
Outline

## Slide 38
Analysis of oscillatory response activities
Phase-amplitude coupling
Time-resolved spike-to-LFP phase locking analysis
Advanced Topics

## Slide 39
Additive response
Phase resetting
Analysis of Response | response types
Mazaheri and Jensen (2010) Front. Hum. Neurosci. 4:177
: amplitude increase
: no amplitude change, but phase reset
Trigger event
Event triggered average
Trials

## Slide 40
Evoked response: fixed latency  phase coherence across trials
Induced response: jitter in latency  no phase coherence across trials
Analysis of Response | response types
Tallon-Baudry and Bertrand (1999) Trend Cogn Sci 3:151-162

## Slide 41
Analysis of Response | response types
Response type |  | Amplitude Increase | Phase coherence
Phase resetting |  |  | 
Additive | Evoked |  | 
 | Induced |  | 

## Slide 42
Analysis of Response | coherence measure
Inter-trial phase coherence (IPC)

## Slide 43
Analysis of Response | coherence measure
Inter-trial phase coherence (IPC)

## Slide 44
Analysis of Response | example
Eye movement related LFP modulation in macaque V1
Amplitude modulation
Time from saccade onset (ms)
Inter-saccade phase
coherence
Event triggered average
Ito et al. (2013) Front. Syst. Neurosci. 7:1
Phase resetting
Phase resetting
Evoked additive
Evoked additive
Induced additive
Induced additive

## Slide 45
Phase-amplitude coupling (PAC)
  modulation of the amplitude of a fast frequency component coherent with the phase of a slow frequency component
Phase-amplitude coupling | definition
Jensen and Colgin (2007) Trends Cogn. Sci. 11:267-9

## Slide 46
Mean vector length (MVL)
Phase-amplitude coupling | PAC measure
Mean vector length (MVL)
Composite signal:

## Slide 47
Mouse barrel cortex LFP oscillations linked to respiration
Phase-amplitude coupling | example
Ito et al. (2014) Nat. Commun. 5:3572

## Slide 48
Phase-amplitude coupling | example
Ito et al. (2014) Nat. Commun. 5:3572
1
2
4
8
16
32
64
128
256
Frequency for amplitude (Hz)
Mean vector length

## Slide 49
Temporal relation between LFP and firing rate
Phase Locking Analysis | spike-to-LFP locking

## Slide 50
Phase Locking Analysis | spike-to-LFP locking

## Slide 51
Phase Locking Analysis | spike-to-LFP locking
Spike-to-LFP phase locking value (PLV)

## Slide 52
Time resolved spike-to-LFP phase locking analysis
  phase locking calculated separately for first and second spikes after fixation onset
Phase Locking Analysis | example
Surprise of PLV
Ito et al. (2011) Cereb. Cortex 21:2482-97